## Slide 1: Water How we use it, Where we get it, What it is worth to us. David Johnson USACE, Vicksburg District Presented to the Association of Levee Boards of Louisiana 5 May 2016
Notes: This presentation covers how the world uses water, what sources of water are used, what is happening to those sources, and the economic impact that water use has to our economy.

## Slide 2: On average we drink 4 liters of water a day, but the food we eat each day requires 2000 liters of water to produce. We are currently mining both ancient and alluvial water to produce the food needed to feed the world, where will the water come from in the future?

## Slide 3
Wheat 500 l/lb
Corn 409 l/lb
Rice 1700 l/lb
Soybeans 818 l/lb
Website: The Hidden Water We Use
How Much Water is Embedded in Everyday Life?
These four crops account for 45.5%
of water consumption
MAV 142 gal/lb
MAV 50 gal/lb
MAV 150 gal/lb

## Slide 4: Water Use by crop and meat product
National Geographic
Pork 2182 l/lb
Chicken 1773 l/lb
Beef 6810 l/lb

## Slide 5: World Water Consumption by Product Categories
Mekonnen, M.M. and Hoekstra, A.Y., 2011. National Water Footprint Accounts: The Green, Blue, and Grey Water Footprint of Production and Consumption, Value of Water Research Report Series No. 50., United Nations Educational, Scientific and Cultural Organization – Institute of Water Education (UNESCO-IHE).
1385 m3/cap/yr
92% Agriculture – 4.5% Industrial Production – 3.5% Domestic Water Supply

## Slide 6: Water Footprint of National Consumption for Countries > 5 Million
Mekonnen, M.M. and Hoekstra, A.Y., 2011. National Water Footprint Accounts: The Green, Blue, and Grey Water Footprint of Production and Consumption, Value of Water Research Report Series No. 50., UNESCO-IHE.
World average (1385 m3/yr/cap)
USA
China
Japan

## Slide 7: Categories of Global Water Sources
Green Water – Precipitation
Blue Water – Surface water and renewable groundwater
Dark Blue Water – Non-renewable groundwater
White -- Interbasin transfers

## Slide 8: World Water Use
Precipitation
Renewable groundwater

## Slide 9: Future World Water Use
Chart: 
Wikipedia: World population based on U.N. estimates. (Units are km3/year)
Assumes that there is sufficient additional land available for crops
2015
Precipitation and surface water
Renewable groundwater

## Slide 10: World Water Footprint by Country
Mekonnen, M.M. and Hoekstra, A.Y., 2010. The green, blue, and grey water footprint of crops and derived crop products, Value of Water Research Report Series No. 47., UNESCO-IHE.
Chart: 
| India | China | USA | Brazil | Russia | Indonesia | Nigeria | Argentina | Canada | Pakistan
Green | 716 | 623.9 | 612 | 303.7 | 304.8 | 285.5 | 190.6 | 157.6 | 120.3 | 40.6
Blue | 231.4 | 118.9 | 95.9 | 8.9 | 10.4 | 11.5 | 1.1 | 4.3 | 1.6 | 74.3
Grey | 99.7 | 223.8 | 118.2 | 16 | 11.6 | 20.9 | 0.6 | 5 | 18.2 | 21.8
World Population (2008) | Millions
China | 1,333.00
India | 1,140.00
United States | 304.00
Indonesia | 228.00
Brazil | 192.00
Pakistan | 166.00
Bangladesh | 160.00
Nigeria | 151.00
Russia | 142.00
Japan | 128.00
World Total | 6,688.00
Units are Gm3/yr or Km3/yr

## Slide 11: World Water Footprint by Basin
Mekonnen, M.M. and Hoekstra, A.Y., 2010. The green, blue, and grey water footprint of crops and derived crop products, Value of Water Research Report Series No. 47., UNESCO-IHE.
Chart: 
| Mississippi | Ganges | Yangtze | Indus | Parana | Niger | Nile | Nuang He | Nelson | Danube | Krishna | Volga | Ob
Green | 424 | 260 | 177 | 102 | 237 | 186 | 131 | 80 | 108 | 106 | 89 | 101 | 92
Blue | 40 | 108 | 18 | 117 | 3.2 | 1.7 | 29 | 21 | 1.5 | 1.8 | 21 | 3.4 | 1.8
Grey | 70 | 39 | 61 | 34 | 9.4 | 0.5 | 6.9 | 31 | 18 | 11 | 8.7 | 3.9 | 1.8

## Slide 12: World Water Use by Crop
Mekonnen, M.M. and Hoekstra, A.Y., 2010. The green, blue, and grey water footprint of crops and derived crop products, Value of Water Research Report Series No. 47., UNESCO-IHE.
Chart: 
| Wheat | Maize | Rice | Apples | Soybean | Sugarcane | Coffee | Rapeseed | Cotton
Green | 760 | 597 | 679 | 33 | 351 | 180 | 108 | 66 | 132
Blue | 204 | 51 | 202 | 8 | 12 | 74 | 1 | 9 | 75
Grey | 123 | 122 | 111 | 7 | 6 | 17 | 4 | 13 | 25
Km3/yr

## Slide 13: Aquifer Foot Prints
Gleeson, T. et al., 2012. ‘Water balance of global aquifers revealed by groundwater footprint,’ Nature, Vol. 488
Aquifer Foot Print = the area needed to recharge the aquifer at the current rate of use and current rate of recharge.

## Slide 14: Where we get our water, and how much we use from aquifers in the U.S.

## Slide 15: Principal Aquifers in the U.S.
USGS Circular 1279, Estimated Withdrawals from Principal Aquifers in the United States, 2000.
Notes: Blue is alluvial sand and gravel, yellow are semi-consolidated sand, brown are karst (limestone), green are sandstone, purple are limestone and sandstone, red are igneous (volcanic and basaltic.

## Slide 16: Groundwater use in the U.S.
USGS Circular 1279, Estimated Withdrawals from Principal Aquifers in the United States, 2000.
Chart: 
| Irrigation | Public Supply | Self-supplied Industrial
 | 56900 | 16000 | 3570
4.7%
20.9%
74.4%
MGD

## Slide 17: Groundwater use in the U.S. by aquifer
USGS Circular 1279, Estimated Withdrawals from Principal Aquifers in the United States, 2000.
Chart: 
| High Plains | Central Valley | Mississippi River alluvial | Basin and Range basin-fill | Floridan | Glacial sand and gravel | California Coastal Basin | Snake River Plain basaltic-rock | Coastal lowlands | Alluvial aquifers | Rio Grande | Northern Atlantic Coastal Plain | Mississippi Embayment | Columbia Plateau basaltic-rock | Pacific Northwest basin-fill | Southeastern Coastal Plain | Biscayne | Edwards-Trinity | Surficial aquifer system | Pacific Northwest basaltic-rock
 | 17500 | 9810 | 9290 | 5620 | 3640 | 3620 | 3440 | 2610 | 2370 | 1800 | 1120 | 1040 | 946 | 933 | 865 | 860 | 812 | 740 | 650 | 475
MGD

## Slide 18: Cumulative groundwater depletion in 40 aquifers, 1900-2008
USGS Scientific Investigations Report 5079, 2013, Groundwater Depletion in the United States (1900-2008).
Km3

## Slide 19: Mississippi Alluvial Aquifer

## Slide 20: Groundwater use in the Mississippi Alluvial Aquifer
USGS Circular 1279, Estimated Withdrawals from Principal Aquifers in the United States, 2000.
Chart: 
| Arkansas | Louisiana | Mississippi | Missouri | Tennessee
Irrigation | 6320 | 221 | 1310 | 1300 | 1.34
Public | 40.5 | 7.27 | 10.4 | 11.7 | 0
Industry | 5.74 | 54.3 | 6.69 | 3.68 | 0
MGD

## Slide 21: Percent of Crops Irrigated in the Mississippi Alluvial Aquifer
Arkansas | Percent Irrigated |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans | Total
2012 | 78.5 | 72.1 | 100.0 | 74.6 | 81.3
2007 | 84.3 | 80.4 | 100.0 | 66.9 | 82.9
2002 | 70.6 | 77.1 | 100.0 | 59.8 | 76.9
1997 | 70.3 | 61.0 | 100.0 | 45.8 | 69.3
Louisiana | Percent Irrigated |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans | Total
2012 | 67.2 | 40.1 | 100.0 | 50.4 | 73.9
2007 | 51.6 | 37.6 | 100.0 | 40.6 | 55.5
2002 | 36.8 | 40.3 | 100.0 | 29.8 | 49.3
1997 | 36.2 | 32.2 | 100.0 | 16.5 | 45.2
Mississippi | Percent Irrigated |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans | Total
2012 | 68.1 | 63.2 | 100.0 | 57.9 | 63.1
2007 | 54.2 | 63.4 | 100.0 | 42.8 | 53.5
2002 | 39.6 | 51.0 | 100.0 | 37.9 | 48.7
1997 | 43.8 | 45.6 | 100.0 | 28.4 | 40.1
Missouri | Percent Irrigated |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans | Total
2012 | 59.1 | 61.8 | 100.0 | 38.3 | 53.5
2007 | 56.1 | 52.4 | 100.0 | 33.7 | 48.9
2002 | 54.0 | 52.0 | 100.0 | 30.2 | 45.5
1997 | 59.3 | 35.6 | 100.0 | 24.5 | 38.8
Based on reports from the USDA, National Agricultural Statistics Service (NASS)

## Slide 22: Conjunctive Water Use Issues in the Mississippi Alluvial Valley
How much can we save through conservation?
Regardless of the above answer- the current rate of aquifer utilization is not sustainable.
New water supplies must be developed to meet the future demand for water.
No single state or federal agency is in charge of the aquifer.
The water use laws vary significantly by state.
The states are reluctant to pass laws which might be interpreted as restricting landowner water rights.
The states are reluctant to measure or monitor water use.

## Slide 23: Groundwater depletion occurs when groundwater abstraction exceeds the groundwater recharge over extensive areas for prolonged periods. When persistent groundwater depletion occurs, this leads to falling groundwater levels.

## Slide 24
Groundwater Availability of the Mississippi Embayment, USGS Professional Paper 1785, 2011.
Net loss in storage
> 16,000,000 acre-feet/year
Net change to streams
> 1,400,000 acre-feet/year

## Slide 25
Water level change from predevelopment to 2007 in the Mississippi River alluvial aquifer
Predicted water level change of the dry scenario in the Mississippi River alluvial aquifer to 2038
Groundwater Availability of the Mississippi Embayment, USGS Professional Paper 1785, 2011
50.1 to 100
0.1 to 50
-24.9 to 0
-49.9 to -25
-74.9 to -50
-99.9 to -75
-130 to -100
Change in elevation

## Slide 26
Water level change from predevelopment to 2007 in the middle Claiborne aquifer
Groundwater Availability of the Mississippi Embayment, USGS Professional Paper 1785, 2011
Predicted water level change of the dry scenario in the middle Claiborne aquifer to 2038

## Slide 27: Consequences of declining aquifer levels
Additional pumping costs for crop irrigation
Wells begin to draw air and yield decreases
Availability of water may restrict crop choice
Salt water intrusion can spoil well
Surface streams lose base flow
Aquatic life adversely impacted
Waste load assimilation reduced
Reduced water quality

## Slide 28: How does today’s weather and the predicted changes in weather patterns affect water demands?

## Slide 29
Average Annual Precipitation in the conterminous U.S. for 1980-1997 as determined by the DAYMET model
Healy, R.W., Winter, T.C., LaBaugh, J.W., and Franke, O.L., 2007, Water Budgets: Foundations for Effective Water-Resources and Environmental Management, USGS Circular 1308
Inches
0-22
22.1-37.2
37.3-51.3
51.4-79.6
79.7-279.1

## Slide 30
Potential Evapotranspiration rates and the difference between annual precipitation and evapotranspiration
Healy, R.W., Winter, T.C., LaBaugh, J.W., and Franke, O.L., 2007, Water Budgets: Foundations for Effective Water-Resources and Environmental Management, USGS Circular 1308
0-22.1 inches
22.2-27.9
28.0-34.5
34.6-42.2
42.3-65.4
-63-0
0-12.5
12.6-34.1
34.2-72.3
72.4-262

## Slide 31: Available Precipitation by County
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report
Effective precipitation is the available precipitation that occurs during the crop growing season. The Mississippi Alluvial Valley receives on average 14 inches of precipitation during the crop season, which is less than the ET demand for those months.

## Slide 32: Freshwater Irrigation Withdrawal 2005
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report

## Slide 33: Total freshwater Withdrawal by County
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report

## Slide 34: Mean Groundwater Recharge (inches/yr)
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report

## Slide 35: Freshwater Irrigation Withdrawal 2005
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report

## Slide 36: Irrigation Methods by State
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report

## Slide 37: Changes in irrigated acreage 1985-2005
Electric Power Research Institute,”Water Use for Electricity Generation and Other Sectors: Recent Changes (1985-2005) and Future Projections (2005-2030), 2011 Technical Report

## Slide 38
USDA-Farm Services Agency

## Slide 39: Third National Climate Assessment Predictions on future precipitation patterns in the U.S.

## Slide 40
National Climate Assessment 2012 Report
Reduced precipitation over most of the agricultural areas of the U.S. during the crop season

## Slide 41
National Climate Assessment 2012 Report
Percent Change
Climate change will increase irrigation demand in the Mississippi Alluvial Valley by 180%

## Slide 42: What are the impacts of groundwater abstraction in excess of the rate of recharge?

## Slide 43
Historically the Big Sunflower River at Sunflower, MS was both a gaining and losing stream
Notes: Total phosphorus shows a significant downward trend. 2008 was a very wet year. It had 78 inches of rain. Third and forth quarters of 2009 were also very wet. So wet there was little fall field preparations.

## Slide 44
Currently Big Sunflower River at Sunflower, MS
is a Disconnected Stream
Notes: Total phosphorus shows a significant downward trend. 2008 was a very wet year. It had 78 inches of rain. Third and forth quarters of 2009 were also very wet. So wet there was little fall field preparations.

## Slide 45
Big Sunflower River at Sunflower, MS
Cumulative Frequency by Decade
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
30s | 166 | 172 | 184 | 216 | 250 | 404 | 672 | 816 | 974
40s | 160 | 170 | 182 | 215 | 290 | 498 | 754 | 844 | 970
50s | 85 | 97 | 109 | 152 | 218 | 404 | 694 | 836 | 964
60s | 97 | 108 | 115 | 134 | 186 | 352 | 596 | 779 | 952
70s | 72 | 100 | 114 | 160 | 296 | 520 | 738.5 | 852 | 962
80s | 19 | 37 | 61 | 100 | 229 | 412 | 640 | 817 | 952
90s | 10.9 | 26.6 | 38.3 | 81.1 | 209 | 409.5 | 647 | 802 | 960
2000s | 40.5 | 49.35 | 56.3 | 88.8 | 225.5 | 392 | 648 | 779 | 946
215
Notes: Total phosphorus shows a significant downward trend. 2008 was a very wet year. It had 78 inches of rain. Third and forth quarters of 2009 were also very wet. So wet there was little fall field preparations.

## Slide 46
Big Sunflower River at Sunflower, MS
Annual Minimum Flow
Chart: Minimum Annual Flow
cfs
Year
YMD starts fall flow augmentation
~ 50 cfs
Notes: Total phosphorus shows a significant downward trend. 2008 was a very wet year. It had 78 inches of rain. Third and forth quarters of 2009 were also very wet. So wet there was little fall field preparations.

## Slide 47
Groundwater Level, Mississippi Delta, Leflore County
Chart: 
Notes: Total phosphorus shows a significant downward trend. 2008 was a very wet year. It had 78 inches of rain. Third and forth quarters of 2009 were also very wet. So wet there was little fall field preparations.

## Slide 48
Big Sunflower at Sunflower
5-Year Moving Average Flows
Chart: 
Chart: 
Year
cfs
Notes: Total phosphorus shows a significant downward trend. 2008 was a very wet year. It had 78 inches of rain. Third and forth quarters of 2009 were also very wet. So wet there was little fall field preparations.

## Slide 49: Groundwater depletion leads to increased capture of exogenous surface water and groundwater through a reduction in groundwater discharge to streams

## Slide 50
Recharge
0.307/248,889
Mississippi River
0.011/ 8,918
Bluff Hills
0.052/ 42,157
Underlying Units
-0.022/-17,836
Discharge to wells
-2.19/-1,775,462
Stream Leakage
0.120/ 97,286
Water-Table Conditions in 2007
How have water-level declines changed the condition of the alluvial aquifer?
Mississippi
River
-0.002/ -1,621
Bluff Hills
0.035/ 28,375
Underlying Units
0.095/77,018
Recharge
0.066/53,507
Stream Leakage
-0.192/ -155,657
Confined Conditions in 1870
(Predevelopment)
This information was provided by the USGS
Notes: Units white text in km3, orange in acre feet

## Slide 51
Chart: 
| Mississippi River | Interior Rivers and Lakes | Bluff Hills | Areal Recharge | Non-storage recharge component (percent of total)
Sumner and Wasson, 1984, 1990 (1983) | 0.47503 | 0.09866 | 0.20706 | 0.21924
Ackerman, 1996 (MS MRVA, 1987) | 0.1353 | 0.087092 | 0 | 0.7776
Arthur, 2001 (1996) | 0 | 0.07122 | 0.068293 | 0.86049
Barlow and Clark, 2011 (MS MRVA, 2007) | 0.10714 | 0.32143 | 0.071429 | 0.5
USGS

## Slide 52
Summer Flow Duration by Decade for Bayou Meto at Lonoke, AR
Based on stage data of the USGS
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
1960 | 0 | 2.6 | 6 | 12 | 26 | 57 | 176 | 410 | 1130
1970 | 4 | 6.75 | 9 | 15 | 31 | 58.5 | 199.5 | 587.5 | 1690
1980 | 0.1 | 0.6 | 1.15 | 5.05 | 15 | 51 | 163 | 427 | 1540
1990 | 0 | 0.2 | 0.6 | 3.5 | 15.5 | 49 | 145 | 248 | 381
2000 | 0 | 0.1 | 0.5 | 4.2 | 20 | 82.5 | 207.5 | 256.5 | 475

## Slide 53
Annual Flow Duration for Boeuf River at Girard, LA
Based on discharge data of the USGS
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
1930 | 30 | 41 | 41 | 62 | 91 | 607 | 1860 | 1990 | 2260
1940 | 36 | 64 | 76 | 116 | 454 | 1180 | 1830 | 2240 | 2650
1950 | 47 | 60 | 70 | 94 | 156.5 | 499 | 1330 | 1740 | 2260
1960 | 15 | 22 | 27 | 44 | 78 | 150 | 344 | 562 | 1570
1970 | 11 | 16 | 19 | 27 | 53 | 163 | 484 | 868 | 1470
1980 | 2.5 | 5.5 | 8 | 13 | 29 | 105 | 400 | 782 | 1380
1990 | 0 | 0.4 | 2.8 | 11 | 29 | 103 | 396 | 773 | 1420
2000 | 0 | 2.3 | 4.8 | 15 | 36 | 111 | 476 | 834 | 1420
2010 | 0 | 0 | 0.2 | 3.2 | 15 | 64 | 272 | 597 | 1080

## Slide 54
Fall Flow Duration for the Boeuf River at Girard, LA by Decade
Based on stage data of the USGS
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
1940 | 33 | 39 | 45 | 75 | 92 | 188 | 513 | 1140 | 1750
1950 | 46 | 52 | 58 | 67 | 100 | 145 | 344 | 890 | 1850
1960 | 14 | 19 | 22 | 28 | 46 | 72 | 103.5 | 166 | 371
1970 | 11 | 14 | 17 | 21 | 34 | 52 | 159 | 283 | 778
1980 | 2.7 | 6 | 8 | 10 | 18 | 41 | 228 | 500 | 1070
1990 | 0.1 | 0.2 | 1 | 4.4 | 13 | 32 | 91 | 195 | 468
2000 | 0.1 | 0.2 | 2.7 | 7.5 | 21 | 55 | 440 | 1010 | 1740

## Slide 55
Flow Duration for Bayou Bartholomew at Jones, AR
Based on discharge data of the USGS
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
1950 | 166 | 188 | 240 | 382 | 1335 | 2640 | 4800 | 5290 | 5600
1960 | 42 | 61 | 74 | 142 | 392 | 1380 | 2920 | 4030 | 6060
1970 | 60 | 91 | 111 | 205 | 607.5 | 2360 | 4130 | 4920 | 5980
1980 | 20 | 50 | 66 | 131 | 659 | 2220 | 3720 | 4960 | 6450
1990 | 19 | 36 | 62 | 153 | 573 | 2080 | 4060 | 5620 | 6800
2000 | 9.8 | 25 | 44 | 123 | 650 | 1980 | 3920 | 5100 | 6370
2010 | 2.1 | 11 | 24 | 69 | 200 | 1170 | 2780 | 4540 | 5630
1335

## Slide 56
Flow Duration for Bayou Macon at Delhi, LA
Based on discharge data of the USGS
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
1940 | 67 | 81 | 119 | 212 | 585 | 1510 | 2870 | 3630 | 4510
1950 | 50 | 88 | 104 | 169 | 532 | 1460 | 2940 | 3400 | 4070
1960 | 48 | 87 | 114 | 163 | 300 | 833 | 1940 | 2900 | 5460
1970 | 96 | 122 | 153 | 255 | 568 | 1750 | 3400 | 5000 | 8110
1980 | 10 | 74 | 100 | 141 | 297 | 997 | 2660 | 4180 | 7370
1990 | 16 | 45 | 59 | 107 | 230 | 758.5 | 2480 | 3580 | 7030
500 cfs
230 cfs

## Slide 57
Spring Flow Duration for Tensas River at Tendal, LA
Based on discharge data of the USGS
Chart: 
| 1 | 5 | 10 | 25 | 50 | 75 | 90 | 95 | 99
1930 | 53 | 87 | 111 | 140 | 377 | 971 | 1430 | 1990 | 2480
1940 | 34 | 71.5 | 115.5 | 242 | 487 | 983.5 | 1520 | 1860 | 2280
1950 | 19 | 26 | 38 | 68.5 | 183 | 607 | 1380 | 2000 | 3090
1960 | 13 | 19 | 22 | 45.5 | 176.5 | 639.5 | 1200 | 1785 | 2490
1970 | 16 | 27.5 | 38 | 85.5 | 272.5 | 754.5 | 1500 | 2175 | 2900
1980 | 12 | 16 | 21 | 40 | 207 | 730.5 | 1625 | 2265 | 3500
1990 | 12 | 27 | 35 | 71 | 369 | 838.5 | 1755 | 2190 | 3450
2000 | 6.7 | 10 | 17 | 39 | 152.5 | 508 | 1230 | 1790 | 2710
2010 | 17 | 23 | 28 | 46 | 110 | 290 | 805 | 1140 | 1770

## Slide 58
Economic Impact of Groundwater

## Slide 59
Farm Income from counties within the MAV
 | Louisiana Farm Income |  |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans | SugarCane | Total
2012 | 575,784,445 | 137,150,000 | 129,821,933 | 640,366,016 | 203,556,944 | 1,686,679,338
2007 | 392,498,911 | 150,523,000 | 106,667,071 | 166,990,064 | 140,827,132 | 957,506,178
2002 | 119,131,975 | 126,453,000 | 41,774,388 | 92,589,345 | 142,104,383 | 522,053,091
1997 | 115,059,782 | 289,015,000 | 109,746,842 | 194,248,172 | 127,470,053 | 835,539,849
 | Mississippi Production-Sales |  |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans |  | Total
2,012 | 658,091,080 | 212,143,000 | 127,360,998 | 945,898,220 |  | 1,943,493,297
2,007 | 332,980,932 | 241,688,000 | 156,646,867 | 371,210,710 |  | 1,102,526,509
2,002 | 75,162,282 | 325,305,000 | 69,361,226 | 176,792,253 |  | 646,620,760
1,997 | 59,639,874 | 383,782,000 | 129,912,110 | 328,147,399 |  | 901,481,383
 | Arkansas Production Sales |  |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans |  | Total
2,012 | 801,872,202 | 413,616,000 | 1,364,597,792 | 1,891,888,341 |  | 4,471,974,335
2,007 | 346,134,408 | 456,246,000 | 1,151,787,723 | 864,507,901 |  | 2,818,676,031
2,002 | 64,666,477 | 364,098,000 | 398,362,952 | 520,482,119 |  | 1,347,609,548
1,997 | 49,534,175 | 527,736,000 | 805,055,869 | 681,952,370 |  | 2,064,278,414
 | Missouri Production Sales |  |  |  |  | 
Year | Corn | Cotton | Rice | Soybeans |  | Total
2,012 | 394,108,668 | 187,246,000 | 167,776,718 | 464,103,545 |  | 1,213,234,930
2,007 | 353,562,203 | 163,619,000 | 142,694,756 | 285,205,052 |  | 945,081,012
2,002 | 110,089,366 | 137,123,000 | 38,184,783 | 170,838,160 |  | 456,235,309
1,997 | 130,360,886 | 176,870,000 | 64,511,226 | 215,264,167 |  | 587,006,279

## Slide 60
Farm Income from counties within the MAV
Year | Corn | Cotton | Rice | Soybeans | SugarCane | Total Value
2,012 | 2,429.9 | 950.2 | 1,789.6 | 3,942.3 | 203.6 | 9,315.4
2,007 | 1,425.2 | 1,012.1 | 1,557.8 | 1,687.9 | 140.8 | 5,823.8
2,002 | 369.1 | 953.0 | 547.7 | 960.7 | 142.1 | 2,972.5
1,997 | 354.6 | 1,377.4 | 1,109.2 | 1,419.6 | 127.5 | 4,388.3
Millions of $

## Slide 61: Conclusion The challenge of the last century was to provide economic security to the MAV, through the reduction in flood risk. That challenge was met. The challenge of this century will be to provide continued economic security by ensuring adequate water supply for crop production. Of the major U.S. aquifers used for irrigation, only the MAV has the potential for recovery (excess precipitation).

## Slide 62: Conclusion – continued Groundwater depletion is a problem not just in the U.S., but in the whole world. The world’s population will continue to grow for the next 50 years or more. The population explosion will increase the demand for food, while increasing the demand on the over stressed aquifers of the world. You met the challenge of the last century, but are you willing to accept the challenge of this century?