## Slide 1: Floodplain Management Principles & Tools for NFIP Compliance
Understanding The Regulatory Process
Pam Lightfoot, CFM
Pamela.Lightfoot@la.gov
225.379.3005

## Slide 2: Objectives
Core NFIP goals
Key floodplain management concepts
Using FIRMs/FIS/BFEs
Ordinance requirements
Permitting & compliance tools
Common compliance issues
Available FEMA resources & map-change processes
Notes: By the end of this presentation, you will understand: the core goals of the NFIP; key concepts of floodplain management; how FIRMs, FISs & BFEs are used along with some community responsibilities and common issues.

## Slide 3: The NFIP at a Glance
Established 1968, administered by FEMA
There are three main parts to the NFIP:
  Floodplain management
  Insurance
  Mapping
Community participation is voluntary but required for residents to buy flood insurance
Local enforcement is the backbone of the program
Notes: In 1968, Congress passed the National Flood Insurance Act to correct some of the shortcomings of traditional flood control and flood relief programs. The act created the National Flood Insurance Program (NFIP).
There are three main parts to the NFIP:
The NFIP underwrites flood insurance coverage only in those communities that adopt and enforce floodplain regulations that meet or exceed NFIP criteria.
Flood insurance is made available to anyone who wants to purchase a policy.
3. Maps of the floodplain are used by communities, insurance agents and lenders.
Although participation is voluntary, it is required in order for the availability of flood insurance as well as the eligibility for other sources of Federal Aid, such as federally guaranteed or insured mortgages (VA, FHA, SBA), Community Development Block Grant Funds, Federal Disaster Assistance, etc.
LA Revised Statute 38:84 authorizes parishes and municipalities to adopt ordinances and regulations to comply with the federal National Flood Insurance Act. This allows them to implement zoning and land use regulations to minimize flood losses and secure flood insurance coverage for their citizens.
Local enforcement is the backbone of the program.

## Slide 4: Purpose & Benefits of Joining the NFIP
Purpose:
  Reduce loss of life and property
  Minimize disruption from flood events
  Promote resilient development
Benefits:
  Purchase of affordable flood insurance
  Eligibility for other sources of Federal Aid
Notes: Communities join the NFIP to make flood insurance available, reduce flood risk and increase resilience. Residents benefit by gaining access to federally backed flood insurance and by living in a community that manages its flood risk responsibly.

## Slide 5: The Special Flood Hazard Area (SFHA)
Areas subject to a 1% annual chance flood (100-year flood)
Zones A, AE, AH, AO, VE, V
Development in the SFHA triggers NFIP requirements
Mandatory purchase of flood insurance
Notes: The land area covered by the floodwaters of the base flood is the 100-year floodplain. This floodplain is called the Special Flood Hazard Area (SFHA).
The SFHA is the area where NFIP floodplain management regulations must be enforced by the community and where the mandatory flood insurance purchase requirement applies.

## Slide 6: Understanding Flood Insurance Rate Maps (FIRMs)
Flood Risk Zones
Base Flood Elevations (BFEs)
Floodways/Coastal Areas
Used for Compliance and Insurance Requirements
Resources:
  FEMA Map Service Center (MSC)
  FEMA National Flood Hazard Layer (NFHL) Viewer
  FEMA FIRMette Tool
Notes: FIRMs identify flood risk zones; shows the base flood elevations (BFEs), if applicable; display floodways, coastal zones, and map panels. They guide permitting and the determination of mandatory purchase of flood insurance.
The Map Service Center and the National Flood Hazard Layer Viewer are ways to access the FIRMs. This site allows you to make a FIRMette, which is a custom, printable section of a large FIRM panel. The FIRMette tool allows people to get a smaller, more manageable version of a flood map that fits on standard paper sizes, making it easier to view and print an area of interest for purposes like flood insurance or floodplain management.

## Slide 7: Understanding Flood Insurance Study (FIS) Reports
Supports & Explains FIRMs (engineering data, floodway tables, profiles, et.)
Determines Flood Risk
Establishes BFEs
Guides Development
Notes: A FEMA Flood Insurance Study (FIS) is a report that compiles and presents flood risk data for a community, providing the detailed engineering analysis that supports the official Flood Insurance Rate Maps (FIRMs). It is used to establish base flood elevations, identify special flood hazard areas, and serve as the basis for community floodplain management and flood insurance requirements under the NFIP.

## Slide 8: Base Flood Elevation (BFE)
The predicted water surface elevation for 1% chance flood (100-year)
BFEs are the foundation for:
  Elevation requirements
  Lowest floor compliance
  Flood proofing design
  Letter of Map Change determinations
Derived from the FIS
Three ways to determine a BFE:
  Floodway Data Table in the FIS
  Profile in the FIS
  FIRM
Notes: In order to have common standards, the NFIP adopted a baseline flooding probability. The NFIP calls this standard the “base” flood, which is the predicted water surface elevation during the 1% annual chance flood. This is the flood that has a 1% (1 out of 100) chance of occurring or being exceeded in any given year.
BFEs are the foundation for: Elevation requirements; Lowest floor compliance; Flood proofing design and LOMC determinations.
There are three ways to determine a BFE; the floodway data table, which is the most accurate, the profile is the next best thing and the least accurate is from the FIRM itself. Communities should always use the more accurate Floodway Data Table or the Profile. The FIRM should only be used where there is no profile or to double check that you read the profile correctly.
FEMA’s Elevation Certificate requires that the BFE be entered to the nearest tenth. The FIS is where you get that elevation.

## Slide 9: The Regulatory Floodway
Channel + adjacent land needed to pass the base flood without raising water levels more than 1 foot
No-rise requirement, analysis must be certified by a licensed professional engineer
Strictest NFIP development standard
Notes: A designated (Regulatory) Floodway is determined by “filling” the floodplain beginning at both edges of the floodplain. This “squeezes” the floodwater toward the channel and causes the flood level to rise. Once a 1-foot rise has been reached, the regulatory floodway boundaries are drawn.
No development allowed unless no-rise can be demonstrated.
Regulatory Floodways scare most communities
I’ll argue that most communities should be embracing this concept – to prevent future lawsuits- increasing flow downstream
The reality is that many communities are already doing a version of this in their development code
– Post Dev discharge can not exceed Pre Dev Discharge
It is just good engineering practice or as CFM’s say “Best Practice”
44 CFR 60.3 C (10)

## Slide 10: Community Responsibilities Required by the NFIP
Adopt and enforce compliant ordinances
Issue development permits
Ensure new and substantially improved structures meet elevation requirements
Conduct inspections and enforcement
Maintain all records (elevation certifications, permits, inspections, etc.)
Make substantial damage determinations after a disaster
Notes: The community must adopt and enforce floodplain management regulations based on the data that FEMA provides.
To do this, it must require a permit for all proposed development, including the placement of manufactured homes, in order to determine whether or not the proposed development is in the SFHA.
If the proposed development is for new or substantially improved structures and it is found to be in the SFHA then it must meet the elevation requirement.
Follow-up conversations and inspections are vital to ensure that the applicant adheres to the requirements of the permit. The most effective way to ensure compliance is to inspect the site frequently during construction. An inspection program also puts builders, developers, and property owners on notice that the community insists that projects are completed in compliance with regulations.
Maintain all records pertaining to the provisions of their flood ordinance.
Also, a community is required to make substantial damage determinations after a disaster.

## Slide 11: What Counts as Development and it’s Impact
Development:
  Any man-made change to improved or unimproved real estate
  Buildings/Structures, filling, ditches, grading, dredging, etc.
Impacts:
  Storm water runoff
  Constricts flood flow
  Loss of flood storage areas
  Causes BFE to rise
  Makes flood maps less accurate
Notes: In 44 CFR 59 the definition of development is: any man-made change in improved and unimproved real estate, including but not limited to buildings or other structures*, mining, dredging, filling, grading, paving, excavation or drilling operations or storage of equipment or materials.
*Buildings and other structures include new or substantially improved/damaged residential and commercial, mobile homes, relocation of a building, camps, etc. (including air conditioning units).
Development can have an adverse impact on the floodplain. It replaces the natural vegetation that is used to absorb water. Filling obstructs flood flows, backing up floodwaters onto upstream and adjacent properties. It reduces the floodplain’s ability to store excess water, sending more water downstream and causing floods to rise to higher levels and flow at higher velocities.

## Slide 12: Key Development Standards
Elevation
Anchoring
Materials
Enclosures
Utilities
Substantial Improvement/Substantial Damage (SI/SD) rules
Notes: Based on 44 CFR 60.3, all structures in the SFHA are required to have the lowest floor at or above BFE, or higher if the local community has adopted freeboard. For manufactured homes, in LA, it’s the bottom of the I-Beam instead of the lowest floor.
Both elevated and floodproofed buildings, especially manufactured homes, must be properly anchored to stabilize them against flood forces. This means anchoring the building to its foundation and ensuring that the foundation will not move. Also, small accessory structures and fuel tanks must be anchored.
Whether a building is elevated or floodproofed, it is important that all of the parts exposed to floodwaters (below the BFE) be made of flood-resistant materials.
If a structure is elevated and the area below the BFE is enclosed, this enclosed area can only be used for parking, storage and building access.
Utilities that services the building must be elevated or floodproofed (i.e. water heater, air conditioner, ductwork, floor joists, etc.)
Substantial Improvement/Substantial Damage triggers full compliance.

## Slide 13: Substantial Improvement/Substantial Damage (SI/SD)
Substantial Improvement (SI):
  Improvement cost ≥ 50% of market value
Substantial Damage (SD):
  Cost to repair damage ≥ 50% of market value
Notes: The basic rule is: If the cost of improvements or cost to repair equals or exceeds 50% of the market value of the building, the building must be brought up to current floodplain management standards.
For the purposes of determining SI/SD, however, market value pertains only to the structure in question. It does not pertain to the land, landscaping, or detached accessory structures on the property.
Substantial improvement applies to any reconstruction, rehabilitation, addition, or other improvement to a structure.
For substantial damage, the damage can be from any cause – flood, fire, earthquake, wind, rain, or other natural or human-induced hazard. Also, the rule applies to all buildings in a SFHA regardless of whether the building was covered by flood insurance or whether disaster assistance is available.
The formula for SD uses “cost to repair” and not “cost of repairs”. The cost to repair the structure must be calculated for full repair to the building’s before-damage condition, even if the owner elects to do less.

## Slide 14: Permitting Documents
Applications
Certifications
(Elevation, Floodproofing, No-Rise, V-Zone, etc.)
As-Built Documentation
Inspection Checklists
Notes: Records are vital in case the project is built in violation of the community’s ordinance or the conditions of a permit. They also provide future owners information on the property.
Permit files should contain copies of all records, as appropriate, pertaining to the provisions of their flood ordinance

## Slide 15: Letters of Map Change (LOMC)
Letter of Map Change (LOMC):
  LOMA
  LOMR
  LOMR-F
Conditional Letters :
  CLOMA
  CLOMR
  CLOMR-F
Notes: No map is perfect and no flood situation is static. FEMA maps are based on the best information available at the time the study was completed. The floodplain maps should be updated as better information becomes available or as changes are proposed in the floodplain.
A Letter of Map Change is simply that, a letter that describes the map change. There are three types of letters of map change: Letter of Map Amendment (LOMA) is used for a single structure or lot, when the natural ground is higher than the BFE; Letter of Map Revision (LOMR) is used for a map re-delineation or a new study; and a Letter of Map Revision Based on Fill (LOMR-F) is used when fill is placed to raise the building site.
Conditional letters are used when an applicant submits data to support proposed construction, modifications or conditions that are expected to exist in the future when the project is complete. Note the conditional part of a CLOMA/CLOMR/CLOMR-F states that if a project is constructed as designed, the base flood elevations can be revised or modified (or the property in question can be removed from the SFHA) after the as-built specifications are submitted and the final LOMA/LOMR/LOMR-F has been issued.

## Slide 16: Common Compliance Issues
No Permits
Incorrect Elevations
Noncompliant Enclosures
Noncompliant Utilities
Fill in the Floodways
Poor SI/SD Documentation
Expired or Missing Elevation Certificates
Lack of Recordkeeping
Notes: More info needs to be added for the narration
Enforcing restrictions against conversion of enclosed areas below the BFE to habitable space is a problem for many floodplain administrators. Often, homeowners convert these spaces into bedrooms, recreation rooms, or other living areas long after the original permit for construction has been issued, resulting in a noncompliant structure. One way to help prevent conversions is to have the owner sign a nonconversion agreement.

## Slide 17: Consequences for Noncompliance
Kicked out of the CRS program
Probation
Suspended from NFIP
Notes: FEMA has three recourses for communities that are found to be noncompliant with NFIP regulations.
If a noncompliant community is in the CRS program, FEMA will kick them out of the CRS program.
Then next step would be to put the community on probation, which results in a mandatory $50 annual surcharge for all NFIP policyholders in that community.
If, after a period of probation, a community fails to remedy its program deficiencies, it will be suspended from the NFIP. Suspension means the community is no longer in the NFIP, which prevents new and renewal flood insurance policies, makes homeowners ineligible for federally regulated mortgages and federal grants as well as disaster assistance.

## Slide 18: Floodplain Administrator (Community Support)
NFIP State Coordinator’s Office
FEMA Region VI
Map Service Center Tutorials
FEMA Technical Bulletins
FEMA Guidance publications
Notes: Support can be found by contacting the NFIP State Coordinator’s Office located within LADOTD, FEMA Region 6 or from multiple tutorials, technical bulletins and guidance publications.
These are really support mechanisms for the local FPA. Much of it is technical and CFR based information but anybody can use it.
Really your first line of support is your local floodplain administrator!

## Slide 19: Best Practices
Adopt Freeboard & Other Higher Standards
Train Permitting Staff & Inspectors
Strengthen Enforcement Language
Coordinate with Engineering & Planning Departments
Recordkeeping
Notes: Adopting freeboard and other higher standards are best practices along with training staff, strengthening enforcement language in the ordinance, coordinate with other departments and keeping good records.

## Slide 20: Summary
Floodplain Management is built on:
  Good Maps
  Strong Standards
  Consistent Enforcement
  Strong Documentation
  Compliance Protects:
    Lives
    Property
    Community NFIP Eligibility
    Affordability of Flood Insurance
Notes: The following slides are state support activities

## Slide 21: The State Coordinating Office for the NFIP
DOTD is the State Coordinating Agency for the NFIP
  Liaison between Louisiana’s 318 participating communities and FEMA (Region VI) regarding compliance with the NFIP which is covered in CFR Title 44, Parts 59 and 60
Notes: LADOTD is the liaison between the states 318 participating communities and FEMA (Region VI) regarding compliance with the NFIP.
DOTD provides assistance to local officials with questions regarding NFIP regulations, maps, flood insurance, disaster assistance, and hazard mitigation.

## Slide 22: The NFIP in Louisiana
Policies in Force: 309,163
Premiums Paid: $282,475,242
Total Coverage: $89,987,473,000
Notes: 41% of the flood insurance policies are for properties located in the Special Flood Hazard Area.
59% of the flood insurance policies are for properties located in a No Special Flood Hazard Area or X Zone.

## Slide 23: Community Rating System (CRS)
  FEMA program administered by ISO
  Rewards communities that exceed the NFIP minimum floodplain management standards
  VOLUNTARY Incentive Program
  19 creditable community Activities
  Based on a 10 Class system - 500 pts. per Class
  5% insurance premium discount per Class
What is the Community Rating System?
Notes: The NFIP’s CRS is a voluntary incentive program that recognizes communities for implementing floodplain management practices that exceed the Federal minimum requirements of the NFIP to provide protection from flooding.
Participation in the CRS is voluntary. By participating, communities earn credit points that determine classifications.
There are 10 CRS Classes: Class 1 requires the most credit points and provides the largest flood insurance premium discount (45%) for policyholders, while Class 10 means the community does not participate in the CRS or has not earned the minimum required credit points, and residents receive no premium reduction.
CRS Class Ratings are similar to Fire Ratings for your Homeowners’ Policy. Each lower class receives a 5% decrease in flood insurance premiums.
ISO administers the CRS program and Mrs. Jennifer Rachal is the CRS Specialist for Louisiana.

## Slide 24: CRS in Louisiana
39 communities currently receive a discount
Chart: 
| Class 9 | Class 8 | Class 7 | Class 6 | Class 5 | Class 3
 | 5 | 14 | 15 | 3 | 2 | 1
CRS Class Rating
# of Communities
1
3
3
14
11
7
Notes: Effective October 1, 2025, Jefferson Parish became the first community in the state to receive a Class 3 rating. Flood insurance policyholders in the parish now receive a 35% discount.

## Slide 25: CRS in Louisiana
Over 242,000 (78%) of Louisiana’s Flood Insurance Policies are in CRS Communities
Over $40M in premium savings annual
Chart: 
 | 0.79 | 0.21
Notes: CRS saves Louisiana flood insurance policyholders more than $40 million annually.
Louisiana is ranked in the Top 5 nationwide with 78% of the state’s flood insurance polices located in CRS communities.
Remember the $282,475,242, that’s 15% on average.
That’s 67,163 people who could be enjoying discounts

## Slide 26: The State NFIP Office’s Role in Risk MAP
Cooperating Technical Partner (CTP)
Risk Mapping, Assessment and Planning (Risk MAP)
  FEMA’s process for updating Flood Insurance Rate Maps (FIRMs)
We have been a Cooperating Technical Partner (CTP) since 2015
  This is 100% funded by FEMA
Work with FEMA to release updated flood risk information to communities
Update the CTP Business Plan yearly to FEMA with project priorities based on FEMA’s goals and metrics
Currently have two contracts to assist with CTP/NFIP task orders. The value of the combined contracts is $10 million
Notes: Phase 0 – 3
1 Discoveries
2 Study/Mapping
3 Preliminary
LOMR Delegation – All kinds on benefits to the state by becoming a LOMR Delegate
1.

## Slide 27
Pam Lightfoot, CFM
Louisiana DOTD
Interim NFIP State Coordinator &
CTP Program Manager
(225) 379-3005
Pam.Lightfoot@la.gov
NFIP Contacts
Tatanisha White
Louisiana DOTD CRS Program Manager
Tatanisha.White@la.gov
Jennifer Rachal, CFM
ISO/CRS Specialist
Jennifer.Rachal@verisk.com
Local Floodplain Administrator (FPA)
https://wwwapps.dotd.la.gov/multimodal/public_works/lafloods/Community_Contacts.aspx